## Slide 1: FZU Computing Center
Jiří Chudoba
VS - Meeting with users, 8.12.2022

## Slide 2: Welcome

## Slide 3: Major recent hardware
2020
  dpmpool25 (770 TB: Auger 273 TB + ATLAS 497 TB)
  nfs20 – 23 (4 * 115 TB, Auger)
  cluster minis (Auger): 12 x 1 CPU (16 cores), 64 GB RAM, 1 Gbps, 10.47 HS06/HTcore, 384 jobslots
  luna96-99: 4 servers (2 CPUs, 64 cores, 512 GB RAM)
2021
  virtualization infrastructure
    3 servers virt07-09
    HA disk array 77 TB (raw) SSD
  8 disk servers ds26-33, 4.6 PB raw (3.6 PB ATLAS + 1 PB Fermilab), 36x 16 TB HDD, 2x25 Gbps
  GPU server gpu01, 1x 16-core CPU + NVIDIA A30
  luna100-105: 6 servers (2 CPUs, 64 cores, 1 TB RAM)
2022
  Cisco Nexus 93180YC-FX – main router
  cluster milan: 29 servers (7x4 + 1), 2xCPU AMD Epyc 7543, 32c, 512 GB RAM, 3.84 TB SSD, 17.8 HS06/HTcore, 2278 HS06 per server
  3712 jobslots, 66 kHS06, CERN : Fermilab : Auger = 35 : 13 : 18 kHS06
  cluster phoebe (4 GPU servers, 20 computing servers)
  luna201-206: 6 servers (2 CPUs, 64 cores, 512 GB RAM, GPU A40)

## Slide 4: External resources: IT4I

## Slide 5: New router

## Slide 6: DPM migration
    DPM to dCache migration
      during planned electricity outage from 14.5. to 15.5.2022
      the biggest site migrated until now
      downtime less than 24 hours
      almost transparent to users

## Slide 7: Monitoring
Notes: https://www.farm.particle.cz/status/

## Slide 8: Energy consumption
    increase of price from 1.8 (2.5) + VAT CZK/kWh to 6.8 CZK/kWh from 1.1.2023
    switch off old clusters lilium (2013, 16.5 kW) and malva (2013, 4.2 kW)
    aplex (2014, 7.2 kW) and magic (2016, 10.8 kW) will follow
Chart: 
| Alice | Atlas | Fermilab | Astro
 | 1125.5357 | 5657.2136 | 1255.2441 | 1642.0066
2022-01: 9680 cores
2022-11: 12160 cores
Chart: 
| Alice | Atlas | Fermilab | Astro
 | 1436.781 | 5885.4724 | 1781.3979 | 3056.3486
2023-01: 10272 cores
Chart: 
| Alice | Atlas | Fermilab | Astro
 | 1240.0155 | 4972.9781 | 1689.4879 | 2369.5185

## Slide 9: Energy consumption
    increase of price from 1.8 (2.5) + VAT CZK/kWh to 6.8 CZK/kWh from 1.1.2023
    switch off old clusters lilium (2013, 16.5 kW) and malva (2013, 4.2 kW)
    aplex (2014, 7.2 kW) and magic (2016, 10.8 kW) will follow
      - 38.7 kW = 280 kCZK/month (PUE = 1.5)
Chart: 
| Alice | Atlas | Fermilab | Astro
 | 1125.5357 | 5657.2136 | 1255.2441 | 1642.0066
2022-01: 9680 cores
2023-01: 10272 cores
2023-0x: 7760 cores
Chart: 
| Alice | Atlas | Fermilab | Astro
 | 1240.0155 | 4972.9781 | 1689.4879 | 2369.5185
Chart: 
| Alice | Atlas | Fermilab | Astro
 | 962.2005 | 3800.3431 | 1499.2565 | 1498.1998

## Slide 10
Chart: HS06 evolution
| 2022-01 | 2022-06 | 2023-01 | 2023-02
 | 84975.405 | 158837.645 | 137971.725 | 112041.535
 | 100 | 186.9219 | 162.3667 | 131.8517

## Slide 11: Miscellaneous
    plans for OS change from CentOS7 to Rocky9
      singularity (apptainer) containers
    Metacentrum: Debian11
    dCache for NFS servers?

## Slide 12: Thank you for your attention